CARMIX 2.0 T

SELF LOADING MOBILE CONCRETE MIXER

CHASSIS:

4 CYLINDERS PERKINS DIESEL ENGINE HP 60 (KW 44,7) WATERCOOLED.

4 WHEEL DRIVE.

DIFFERENTIAL AXLES WITH PLANETARY REDUCERS ON 4 WHEELS HYDROSTATIC TRANSMISSION.

TWIN INDEPENDENT BRAKE CIRCUIT WITH OIL BATH DISC BRAKES ACTING ON 4 WHEELS. PARKING BRAKE.

12 VOLTS ELECTRIC PLANT FOR STARTER,

SERVICE AND LIGHTING.

ROPS FOPS CANOPY.

REVOLVING DRIVING SEAT WITH AUTOMATIC INVERSION OF HYDRAULIC STEERING CIRCUIT.

SAFETY SWITCH-OFF BATTERY.

MIXING DRUM:

CAPACITY 2800 LITRES. REAL CONCRETE YIELD 2 CUBIC METERS

DISCHARGING BY REVERSING DRUM ROTATION.

ELECTRIC SERVOCONTROL FOR MIXING AND DISCHARGING.

SELF-LOADING BATCHING SHOVEL:

CAPACITY 300 LITRES. HYDRAULIC GATE.

WATER SYSTEM:

SELF-PRIMING PUMP HYDRAULICALLY OPERATED.

WATER METER. TWO TANKS TOTAL CAPACITY ABOUT 450 LITRES.

DISCHARGING CHUTE:

SLEWING THROUGH 180°. ONE EXTENSION. HYDRAULIC TILTING.

| OPTIONAL EQUIPMENT ON REQUEST: |  |
| --- | --- |
| - | ADDITIONAL DISCHARGING CHUTE EXTENSION | EURO |  |
| - | SPARE WHEEL | EURO |  |