CARMIX 3.5 T

SELF LOADING MOBILE CONCRETE MIXER WITH “SLEWING” DRUM

CHASSIS:

4 CYLINDERS DIESEL ENGINE PERKINS TURBO 107 HP WATERCOOLED.

4 WHEEL DRIVE. DIFFERENTIAL AXLES WITH PLANETARY REDUCERS ON 4 WHEELS.

HYDROSTATIC TRANSMISSION WITH 2 SPEEDS FOR WORK AND TRANSFER.

TWIN INDEPENDENT BRAKE CIRCUIT WITH OIL BATH DISC BRAKES ACTING ON 4 WHEELS.

NEGATIVE PARKING BRAKE HYDRAULICALLY OPERATED.

12 VOLTS ELECTRIC PLANT FOR STARTER,

SERVICE AND LIGHTING.

FRONT DRIVER CABIN COMPLETE WITH DOOR,

PLACED NEAR THE LOADING SHOVEL. HYDRAULIC STEERING.

JOYMIX: ONE JOYSTICK FOR MAIN HYDRAULIC OPERATIONS (SHOVEL AND DRUM).

SAFETY SWITCH-OFF BATTERY.

“SLEWING” MIXING DRUM:

CAPACITY 4.750 LITRES.

REAL CONCRETE YIELD 3,5 CUBIC mETERS

DRUM MOUNTED ON FIFTH WHEEL.

HYDRAULIC SLEWING THROUGH 300° FOR DISCHARGING CONCRETE AROUND 4 SIDES OF THE VEHICLE AT OVER 2 METRES OF HEIGHT.

DISCHARGING BY REVERSING DRUM ROTATION.

ELECTRIC SERVOCONTROL FOR MIXING AND DISCHARGING.

SELF-LOADING BATCHING SHOVEL:

HYDRAULICALLY OPERATED. CAPACITY 550 LITRES.

HYDRAULIC GATE.

WATER SYSTEM:

SELF-PRIMING PUMP HYDRAULICALLY OPERATED.

WATER METER. TWO TANKS TOTAL CAPACITY ABOUT 800 LITRES.

DISCHARGING CHUTE:

SLEWING THROUGH 180°. ONE EXTENSION. HYDRAULIC TILTING.

| OPTIONAL EQUIPMENT ON REQUEST: |  |
| --- | --- |
| - | ELECTRONIC WEIGHING DEVICE WITH PRINTER |  |  |
| - | ELECTRONIC WEIGHING DEVICE WITHOUT PRINTER |  |  |
| - | HIGH-PRESSURE WASHING PUMP (90 BAR) WITH GUN |  |  |
| - | ADDITIONAL DISCHARGING CHUTE EXTENSION |  |  |
| - | SPARE WHEEL |  |  |